NSF Standard(s) Impacted:	NSF/ANSI 51

Background:
### Provide a brief background statement indicating the cause and nature of concern, the impacts identified relevant to public health, public understanding, etc, and any other reason why the issue should be considered by the Committee. Reference as appropriate any specific section(s) of the standard(s) that are related to the issue.

An information paper on Bisphenols was presented at the Joint Committee Meeting by Mike Kohler on August 9th, 2023. As an action item D. Negandhi volunteered to submit an issue paper to the JC and M. Kohler agreed to help. NSF Staff created an internal report based on a review of various regulations for Bisphenols in the EU, US-FDA and individual states (copy attached).

Recently (April 2024) US-EPA has proposed an extension of the Safe Drinking Water Act restrictions on chemicals to include PFA’s and their derivatives effective 2029 (See attached copy of US-EPA Document). Continued inclusion of these chemicals in the human food chain is detrimental to human health.

Mike Kohler and I propose revisions to the NSF Standard 51 – Food Equipment Materials as noted below.

Recommendation:
Clearly state what action is needed: e.g., recommended changes to the standard(s) including the current text of the relevant section(s) indicating deletions by use of strike-out and additions by highlighting or underlining; e.g., reference of the issue to a Task Group for detailed consideration; etc.

    1. Food zone materials shall not contain lead, arsenic, cadmium, or mercury any of the following as intentional ingredients.

- Lead;
- Arsenic;
- Cadmium;
- Mercury; or
- Bisphenols, including BPA, BPAF, BPF, and BPS
Brass and bronze materials may contain lead as permitted under Section 4.2.3.2.

4.1.3 Food zone materials with formulations reviewed and verified to contain no intentionally added Perfluoroalkyl and polyfluoroalkyl substances (PFAS) may be designated as having “no added PFAS”.

Rationale: Information papers on PFAS and Bisphenols were presented at the 08/2023 JC Meeting. An action to submit an issue paper for restriction of Bisphenols was established. International concerns for health risks associated with Bisphenols has been increasing over the past many years. More recently, concerns on the use of PFAS is growing aggressively but regulations are somewhat inconsistent and in a state of flux. Therefore, this proposal is offering an optional approach for materials without added PFAS to be designated as such. Also, reformatting the structure of this section to a more preferred bullet item list.

NSF/ANSI 170

3.xxx PFAS: Perfluoroalkyl and polyfluoroalkyl substances. Any chemical with at least a perfluorinated methyl group (-CF3) or a perfluorinated methylene group (-CF2-) without any H/Cl/Br/I atom attached to it (OECD 20211 definition). Chemicals considered to be PFAS can be found in the OECD database of PFAS chemicals.

1 Organization for Economic Cooperation and Development. 2, rue André Pascal, 75016 Paris, France. <https://www.oecd.org>

Supplementary Materials (photographs, diagrams, reports, etc.):
If not provided electronically, the submitter will be responsible to have sufficient copies to distribute to committee members.

I hereby grant NSF International the non-exclusive, royalty free rights, including non-exclusive, royalty free rights in copyright; in this item and I understand that I acquire no rights in any publication of NSF International in which this item in this or another similar or analogous form is used.

Signature*:	Dipak J. Negandhi
Company:	Negandhi Technologies
Telephone Number:	601-259-4703	E-mail: djnegandhi@gmail.com
Submission Date:

Signature*:	Mike Kohler
Company:	NSF
Telephone Number:	734-913-5775	E-mail:	kohler@nsf.org
Submission Date:

Please submit to:	Al Rose, arose@nsf.org

*Type written name will suffice as signature